## Slide 1
Chapter 2
Memory Hierarchy Design
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the allusion of a large, fast memory being presented to the processor
Introduction

## Slide 3: Memory Hierarchy
Introduction

## Slide 4: Memory Performance Gap
Introduction

## Slide 5: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references/second
      = 409.6 GB/s!
    DRAM bandwidth is only 8% of this (34.1 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 6: Performance and Power
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget
Introduction

## Slide 7: Memory Hierarchy Basics
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets in cache
Introduction

## Slide 8: Memory Hierarchy Basics
n sets => n-way set associative
  Direct-mapped cache => one block per set
  Fully associative => one set
Writing to cache: two strategies
  Write-through
    Immediately update lower levels of hierarchy
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced
  Both strategies use write buffer to make writes asynchronous
Introduction

## Slide 9: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Introduction

## Slide 10: Memory Hierarchy Basics
Speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses
Introduction

## Slide 11: Memory Hierarchy Basics
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time
Introduction

## Slide 12: Memory Technology and Optimizations
Performance metrics
  Latency is concern of cache
  Bandwidth is concern of multiprocessors and I/O
  Access time
    Time between read request and when desired word arrives
  Cycle time
    Minimum time between unrelated requests to memory
SRAM memory has low latency, use for cache
Organize DRAM chips into many banks for high bandwidth, use for main memory
Memory Technology and Optimizations

## Slide 13: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refeshed
    Every ~ 8 ms (roughly 5% of time)
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)
Memory Technology and Optimizations

## Slide 14: Internal Organization of DRAM
Memory Technology and Optimizations

## Slide 15: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device
Memory Technology and Optimizations

## Slide 16: Memory Optimizations
Memory Technology and Optimizations

## Slide 17: Memory Optimizations
Memory Technology and Optimizations

## Slide 18: Memory Optimizations
DDR:
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1333 MHz
GDDR5 is graphics memory based on DDR3
Memory Technology and Optimizations

## Slide 19: Memory Optimizations
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketted DIMM modules
Memory Technology and Optimizations

## Slide 20: Memory Power Consumption
Memory Technology and Optimizations

## Slide 21: Stacked/Embedded DRAMs
Stacked DRAMs in same package as processor
  High Bandwidth Memory (HBM)
Memory Technology and Optimizations

## Slide 22: Flash Memory
Type of EEPROM
Types: NAND (denser) and NOR (faster)
NAND Flash:
  Reads are sequential, reads entire page (.5 to 4 KiB)
  25 us for first byte, 40 MiB/s for subsequent bytes
  SDRAM: 40 ns for first byte, 4.8 GB/s for subsequent bytes
  2 KiB transfer: 75 uS vs 500 ns for SDRAM, 150X slower
  300 to 500X faster than magnetic disk
Memory Technology and Optimizations

## Slide 23: NAND Flash Memory
Must be erased (in blocks) before being overwritten
Nonvolatile, can use as little as zero power
Limited number of write cycles (~100,000)
$2/GiB, compared to $20-40/GiB for SDRAM and $0.09 GiB for magnetic disk
Phase-Change/Memrister Memory
  Possibly 10X improvement in write performance and 2X improvement in read performance
Memory Technology and Optimizations

## Slide 24: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  Use spare rows to replace defective rows
Chipkill: a RAID-like error recovery technique
Memory Technology and Optimizations

## Slide 25: Advanced Optimizations
Reduce hit time
  Small and simple first-level caches
  Way prediction
Increase bandwidth
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty
  Critical word first, merging write buffers
Reduce miss rate
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization
  Hardware or compiler prefetching
Advanced Optimizations

## Slide 26: L1 Size and Associativity
Access time vs. size and associativity
Advanced Optimizations

## Slide 27: L1 Size and Associativity
Energy per read vs. size and associativity
Advanced Optimizations

## Slide 28: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty
Advanced Optimizations

## Slide 29: Pipelined Caches
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 30: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 31: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty
Advanced Optimizations

## Slide 32: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 33: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
Advanced Optimizations
No write buffering
Write buffering

## Slide 34: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses
Advanced Optimizations

## Slide 35: Blocking
for (i = 0; i < N; i = i + 1)
for (j = 0; j < N; j = j + 1)
{
r = 0;
for (k = 0; k < N; k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = r;
};

## Slide 36: Blocking
for (jj = 0; jj < N; jj = jj + B)
for (kk = 0; kk < N; kk = kk + B)
for (i = 0; i < N; i = i + 1)
for (j = jj; j < min(jj + B,N); j = j + 1)
{
r = 0;
for (k = kk; k < min(kk + B,N); k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = x[i][j] + r;
};

## Slide 37: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 38: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 39: Use HBM to Extend Hierarchy
128 MiB to 1 GiB
Smaller blocks require substantial tag storage
Larger blocks are potentially inefficient
One approach (L-H):
  Each SDRAM row is a block index
  Each row contains set of tags and 29 data segments
  29-set associative
  Hit requires a CAS
Advanced Optimizations

## Slide 40: Use HBM to Extend Hierarchy
Another approach (Alloy cache):
  Mold tag and data together
  Use direct mapped
Both schemes require two DRAM accesses for misses
  Two solutions:
    Use map to keep track of blocks
    Predict likely misses
Advanced Optimizations

## Slide 41: Use HBM to Extend Hierarchy
Advanced Optimizations

## Slide 42: Summary
Advanced Optimizations

## Slide 43: Virtual Memory and Virtual Machines
Protection via virtual memory
  Keeps processes in their own memory space
Role of architecture
  Provide user mode and supervisor mode
  Protect certain aspects of CPU state
  Provide mechanisms for switching between user mode and supervisor mode
  Provide mechanisms to limit memory accesses
  Provide TLB to translate addresses
Virtual Memory and Virtual Machines

## Slide 44: Virtual Machines
Supports isolation and security
Sharing a computer among many unrelated users
Enabled by raw speed of processors, making the overhead more acceptable
Allows different ISAs and operating systems to be presented to user programs
  “System Virtual Machines”
  SVM software is called “virtual machine monitor” or “hypervisor”
  Individual virtual machines run under the monitor are called “guest VMs”
Virtual Memory and Virtual Machines

## Slide 45: Requirements of VMM
Guest software should:
  Behave on as if running on native hardware
  Not be able to change allocation of real system resources
VMM should be able to “context switch” guests
Hardware must allow:
  System and use processor modes
  Privileged subset of instructions for allocating system resources
Virtual Memory and Virtual Machines

## Slide 46: Impact of VMs on Virtual Memory
Each guest OS maintains its own set of page tables
  VMM adds a level of memory between physical and virtual memory called “real memory”
  VMM maintains shadow page table that maps guest virtual addresses to physical addresses
    Requires VMM to detect guest’s changes to its own page table
    Occurs naturally if accessing the page table pointer is a privileged operation
Virtual Memory and Virtual Machines

## Slide 47: Extending the ISA for Virtualization
Objectives:
  Avoid flushing TLB
  Use nested page tables instead of shadow page tables
  Allow devices to use DMA to move data
  Allow guest OS’s to handle device interrupts
  For security: allow programs to manage encrypted portions of code and data
Virtual Memory and Virtual Machines

## Slide 48: Fallacies and Pitfalls
Predicting cache performance of one program from another
Simulating enough instructions to get accurate performance measures of the memory hierarchy
Not deliverying high memory bandwidth in a cache-based system