## Slide 1
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
Beyond this, there are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMP processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
Introduction

## Slide 3: Instruction-Level Parallelism
When exploiting instruction-level parallelism, goal is to maximize CPI
  Pipeline CPI =
    Ideal pipeline CPI +
    Structural stalls +
    Data hazard stalls +
    Control stalls
Parallelism with basic block is limited
  Typical size of basic block = 3-6 instructions
  Must optimize across branches
Introduction

## Slide 4: Data Dependence
Loop-Level Parallelism
  Unroll loop statically or dynamically
  Use SIMD (vector processors and GPUs)
Challenges:
  Data dependency
    Instruction j is data dependent on instruction i if
      Instruction i produces a result that may be used by instruction j
      Instruction j is data dependent on instruction k and instruction k is data dependent on instruction i
Dependent instructions cannot be executed simultaneously
Introduction

## Slide 5: Data Dependence
Dependencies are a property of programs
Pipeline organization determines if dependence is detected and if it causes a stall
Data dependence conveys:
  Possibility of a hazard
  Order in which results must be calculated
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect
Introduction

## Slide 6: Name Dependence
Two instructions use the same name but no flow of information
  Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use register renaming techniques
Introduction

## Slide 7: Other Factors
Data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
Control Dependence
  Ordering of instruction i with respect to a branch instruction
    Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controlled by the branch
    An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
Introduction

## Slide 8: Examples
or instruction dependent on add and sub
Assume x4 isn’t used after skip
  Possible to move sub before the branch
Introduction
Example 1:
add x1,x2,x3
beq x4,x0,L
sub x1,x1,x6
L: …
or x7,x1,x8
Example 2:
add x1,x2,x3
beq x12,x0,skip
sub x4,x5,x6
add x5,x4,x9
skip:
or x7,x8,x9

## Slide 9: Compiler Techniques for Exposing ILP
Pipeline scheduling
  Separate dependent instruction from the source instruction by the pipeline latency of the source instruction
Example:
  for (i=999; i>=0; i=i-1)
  x[i] = x[i] + s;
Compiler Techniques

## Slide 10: Pipeline Stalls
Loop: fld f0,0(x1)
stall
fadd.d f4,f0,f2
stall
stall
fsd f4,0(x1)
addi x1,x1,-8
bne x1,x2,Loop
Compiler Techniques
Loop: fld f0,0(x1)
addi x1,x1,-8
fadd.d f4,f0,f2
stall
stall
fsd f4,0(x1) bne x1,x2,Loop

## Slide 11: Loop Unrolling
Loop unrolling
  Unroll by a factor of 4 (assume # elements is divisible by 4)
  Eliminate unnecessary instructions
Loop: fld f0,0(x1)
fadd.d f4,f0,f2
fsd f4,0(x1) //drop addi & bne
fld f6,-8(x1)
fadd.d f8,f6,f2
fsd f8,-8(x1) //drop addi & bne
fld f0,-16(x1)
fadd.d f12,f0,f2
fsd f12,-16(x1) //drop addi & bne
fld f14,-24(x1)
fadd.d f16,f14,f2
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
note: number of live registers vs. original loop

## Slide 12: Loop Unrolling/Pipeline Scheduling
Pipeline schedule the unrolled loop:
Loop: fld f0,0(x1)
fld f6,-8(x1)
fld f8,-16(x1)
fld f14,-24(x1)
fadd.d f4,f0,f2
fadd.d f8,f6,f2
fadd.d f12,f0,f2
fadd.d f16,f14,f2
fsd f4,0(x1)
fsd f8,-8(x1)
fsd f12,-16(x1)
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
14 cycles
3.5 cycles per element

## Slide 13: Strip Mining
Unknown number of loop iterations?
  Number of iterations = n
  Goal: make k copies of the loop body
  Generate pair of loops:
    First executes n mod k times
    Second executes n / k times
    “Strip mining”
Compiler Techniques

## Slide 14: Branch Prediction
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
    (m,n) predictor: behavior from last m branches to choose from 2m n-bit predictors
Tournament predictor:
  Combine correlating predictor with local predictor
Branch Prediction

## Slide 15: Branch Prediction
Branch Prediction
gshare
tournament

## Slide 16: Branch Prediction Performance
Branch Prediction

## Slide 17: Branch Prediction Performance
Branch Prediction

## Slide 18: Tagged Hybrid Predictors
Need to have predictor for each branch and history
  Problem: this implies huge tables
  Solution:
    Use hash tables, whose hash value is based on branch address and branch history
    Longer histories may lead to increased chance of hash collision, so use multiple tables with increasingly shorter histories
Branch Prediction

## Slide 19: Tagged Hybrid Predictors
Branch Prediction

## Slide 20: Tagged Hybrid Predictors
Branch Prediction

## Slide 21: Dynamic Scheduling
Rearrange order of instructions to reduce stalls while maintaining data flow
Advantages:
  Compiler doesn’t need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
Disadvantage:
  Substantial increase in hardware complexity
  Complicates exceptions
Dynamic Scheduling

## Slide 22: Dynamic Scheduling
Dynamic scheduling implies:
  Out-of-order execution
  Out-of-order completion
Example 1:
  fdiv.d f0,f2,f4
  fadd.d f10,f0,f8
  fsub.d f12,f8,f14
  fsub.d is not dependent, issue before fadd.d
Dynamic Scheduling

## Slide 23: Dynamic Scheduling
Example 2:
  fdiv.d f0,f2,f4
  fmul.d f6,f0,f8
  fadd.d f0,f10,f14
  fadd.d is not dependent, but the antidependence makes it impossible to issue earlier without register renaming
Dynamic Scheduling

## Slide 24: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d f6,f0,f8
fsd f6,0(x1)
fsub.d f8,f10,f14
fmul.d f6,f10,f8
  name dependence with f6
antidependence
antidependence
Dynamic Scheduling

## Slide 25: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d S,f0,f8
fsd S,0(x1)
fsub.d T,f10,f14
fmul.d f6,f10,T
Now only RAW hazards remain, which can be strictly ordered
Dynamic Scheduling

## Slide 26: Register Renaming
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Dynamic Scheduling

## Slide 27: Register Renaming
RS fetches and buffers an operand as soon as it becomes available (not necessarily involving register file)
Pending instructions designate the RS to which they will send their output
  Result values broadcast on a result bus, called the common data bus (CDB)
Only the last output updates the register file
As instructions are issued, the register specifiers are renamed with the reservation station
May be more reservation stations than registers
Load and store buffers
  Contain data and addresses, act like reservation stations
Dynamic Scheduling

## Slide 28: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 29: Tomasulo’s Algorithm
Three Steps:
  Issue
    Get next instruction from FIFO queue
    If available RS, issue the instruction to the RS with operand values if available
    If operand values not available, stall the instruction
  Execute
    When operand becomes available, store it in any reservation stations waiting for it
    When all operands are ready, issue the instruction
    Loads and store maintained in program order through effective address
    No instruction allowed to initiate execution until all branches that proceed it in program order have completed
  Write result
    Write result on CDB into reservation stations and store buffers
      (Stores must wait until address and value are received)
Dynamic Scheduling

## Slide 30: Example
Dynamic Scheduling

## Slide 31: Tomasulo’s Algorithm
Example loop:
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x16 != x2
Dynamic Scheduling

## Slide 32: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 33: Hardware-Based Speculation
Execute instructions along predicted execution paths but only commit the results if prediction was correct
Instruction commit: allowing an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits
  I.e. updating state or taking an execution
Hardware-Based Speculation

## Slide 34: Reorder Buffer
Reorder buffer – holds the result of instruction between completion and commit
Four fields:
  Instruction type: branch/store/register
  Destination field: register number
  Value field: output value
  Ready field: completed execution?
Modify reservation stations:
  Operand source is now reorder buffer instead of functional unit
Hardware-Based Speculation

## Slide 35: Reorder Buffer
Issue:
  Allocate RS and ROB, read available operands
Execute:
  Begin execution when operand values are available
Write result:
  Write result and ROB tag on CDB
Commit:
  When ROB reaches head of ROB, update register
  When a mispredicted branch reaches head of ROB, discard all entries
Hardware-Based Speculation

## Slide 36: Reorder Buffer
Register values and memory values are not written until an instruction commits
On misprediction:
  Speculated entries in ROB are cleared
Exceptions:
  Not recognized until it is ready to commit
Hardware-Based Speculation

## Slide 37: Reorder Buffer
Hardware-Based Speculation

## Slide 38: Reorder Buffer
Hardware-Based Speculation

## Slide 39: Multiple Issue and Static Scheduling
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions:
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
  Dynamically scheduled superscalar processors
Multiple Issue and Static Scheduling

## Slide 40: Multiple Issue
Multiple Issue and Static Scheduling

## Slide 41: VLIW Processors
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Multiple Issue and Static Scheduling

## Slide 42: VLIW Processors
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
Multiple Issue and Static Scheduling

## Slide 43: Dynamic Scheduling, Multiple Issue, and Speculation
Modern microarchitectures:
  Dynamic scheduling + multiple issue + speculation
Two approaches:
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
Issue logic is the bottleneck in dynamically scheduled superscalars
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 44: Overview of Design
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 45: Multiple Issue
Examine all the dependencies amoung the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Also need multiple completion/commit
To simplify RS allocation:
  Limit the number of instructions of a given class that can be issued in a “bundle”, i.e. on FP, one integer, one load, one store
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 46: Example
Loop: ld x2,0(x1) //x2=array element
addi x2,x2,1 //increment x2
sd x2,0(x1) //store result
addi x1,x1,8 //increment pointer
bne x2,x3,Loop //branch if not last
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 47: Example (No Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 48: Example (Mutiple Issue with Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 49: Branch-Target Buffer
Need high instruction bandwidth
  Branch-Target buffers
    Next PC prediction buffer, indexed by current PC
Adv. Techniques for Instruction Delivery and Speculation

## Slide 50: Branch Folding
Optimization:
  Larger branch-target buffer
  Add target instruction into buffer to deal with longer decoding time required by larger buffer
  “Branch folding”
Adv. Techniques for Instruction Delivery and Speculation

## Slide 51: Return Address Predictor
Most unconditional branches come from function returns
The same procedure can be called from multiple sites
  Causes the buffer to potentially forget about the return address from previous calls
Create return address buffer organized as a stack
Adv. Techniques for Instruction Delivery and Speculation

## Slide 52: Return Address Predictor
Adv. Techniques for Instruction Delivery and Speculation

## Slide 53: Integrated Instruction Fetch Unit
Design monolithic unit that performs:
  Branch prediction
  Instruction prefetch
    Fetch ahead
  Instruction memory access and buffering
    Deal with crossing cache lines
Adv. Techniques for Instruction Delivery and Speculation

## Slide 54: Register Renaming
Register renaming vs. reorder buffers
  Instead of virtual registers from reservation stations and reorder buffer, create a single register pool
    Contains visible registers and virtual registers
  Use hardware-based map to rename registers during issue
  WAW and WAR hazards are avoided
  Speculation recovery occurs by copying during commit
  Still need a ROB-like queue to update table in order
  Simplifies commit:
    Record that mapping between architectural register and physical register is no longer speculative
    Free up physical register used to hold older value
    In other words: SWAP physical registers on commit
  Physical register de-allocation is more difficult
    Simple approach: deallocate virtual register when next instruction writes to its mapped architecturally-visibly register
Adv. Techniques for Instruction Delivery and Speculation

## Slide 55: Integrated Issue and Renaming
Combining instruction issue with register renaming:
  Issue logic pre-reserves enough physical registers for the bundle
  Issue logic finds dependencies within bundle, maps registers as necessary
  Issue logic finds dependencies between current bundle and already in-flight bundles, maps registers as necessary
Adv. Techniques for Instruction Delivery and Speculation

## Slide 56: How Much?
How much to speculate
  Mis-speculation degrades performance and power relative to no speculation
    May cause additional misses (cache, TLB)
  Prevent speculative code from causing higher costing misses (e.g. L2)
Speculating through multiple branches
  Complicates speculation recovery
Speculation and energy efficiency
  Note: speculation is only energy efficient when it significantly improves performance
Adv. Techniques for Instruction Delivery and Speculation

## Slide 57: How Much?
Adv. Techniques for Instruction Delivery and Speculation
integer

## Slide 58: Energy Efficiency
Value prediction
  Uses:
    Loads that load from a constant pool
    Instruction that produces a value from a small set of values
  Not incorporated into modern processors
  Similar idea--address aliasing prediction--is used on some processors to determine if two stores or a load and a store reference the same address to allow for reordering
Adv. Techniques for Instruction Delivery and Speculation

## Slide 59: Fallacies and Pitfalls
It is easy to predict the performance/energy efficiency of two different versions of the same ISA if we hold the technology constant
Fallacies and Pitfalls

## Slide 60: Fallacies and Pitfalls
Processors with lower CPIs / faster clock rates will also be faster
  Pentium 4 had higher clock, lower CPI
  Itanium had same CPI, lower clock
Fallacies and Pitfalls

## Slide 61: Fallacies and Pitfalls
Sometimes bigger and dumber is better
  Pentium 4 and Itanium were advanced designs, but could not achieve their peak instruction throughput because of relatively small caches as compared to i7
And sometimes smarter is better than bigger and dumber
  TAGE branch predictor outperforms gshare with less stored predictions
Fallacies and Pitfalls

## Slide 62: Fallacies and Pitfalls
Believing that there are large amounts of ILP available, if only we had the right techniques
Fallacies and Pitfalls