## Slide 1
Chapter 5
Thread-Level Parallelism
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit
Introduction

## Slide 3: Types
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks
Introduction

## Slide 4: Cache Coherence
Processors may see different values through their caches:
Centralized Shared-Memory Architectures

## Slide 5: Cache Coherence
Coherence
  All reads by any processor must return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
Centralized Shared-Memory Architectures

## Slide 6: Enforcing Coherence
Coherent caches provide:
  Migration: movement of data
  Replication: multiple copies of data
Cache coherence protocols
  Directory based
    Sharing status of each block kept in one location
  Snooping
    Each core tracks sharing status of each block
Centralized Shared-Memory Architectures

## Slide 7: Snoopy Coherence Protocols
Write invalidate
  On write, invalidate all other copies
  Use bus itself to serialize
    Write cannot complete until bus access is obtained
Write update
  On write, update all copies
Centralized Shared-Memory Architectures

## Slide 8: Snoopy Coherence Protocols
Locating an item when a read miss occurs
  In write-back cache, the updated value must be sent to the requesting processor
Cache lines marked as shared or exclusive/modified
  Only writes to shared lines need an invalidate broadcast
    After this, the line is marked as exclusive
Centralized Shared-Memory Architectures

## Slide 9: Snoopy Coherence Protocols
Centralized Shared-Memory Architectures

## Slide 10: Snoopy Coherence Protocols
Centralized Shared-Memory Architectures

## Slide 11: Snoopy Coherence Protocols
Complications for the basic MSI protocol:
  Operations are not atomic
    E.g. detect miss, acquire bus, receive a response
    Creates possibility of deadlock and races
    One solution: processor that sends invalidate can hold bus until other processors receive the invalidate
Extensions:
  Add exclusive state to indicate clean block in only one cache (MESI protocol)
    Prevents needing to write invalidate on a write
  Owned state
Centralized Shared-Memory Architectures

## Slide 12: Coherence Protocols: Extensions
Shared memory bus and snooping bandwidth is bottleneck for scaling symmetric multiprocessors
  Duplicating tags
  Place directory in outermost cache
  Use crossbars or point-to-point networks with banked memory
Centralized Shared-Memory Architectures

## Slide 13: Coherence Protocols
Every multicore with >8 processors uses an interconnect other than bus
  Makes it difficult to serialize events
  Write and upgrade misses are not atomic
  How can the processor know when all invalidates are complete?
  How can we resolve races when two processors write at the same time?
  Solution: associate each block with a single bus
Centralized Shared-Memory Architectures

## Slide 14: Performance
Coherence influences cache miss rate
  Coherence misses
    True sharing misses
      Write to shared block (transmission of invalidation)
      Read an invalidated block
    False sharing misses
      Read an unmodified word in an invalidated block
Performance of Symmetric Shared-Memory Multiprocessors

## Slide 15: Performance Study: Commercial Workload
Performance of Symmetric Shared-Memory Multiprocessors

## Slide 16: Performance Study: Commercial Workload
Performance of Symmetric Shared-Memory Multiprocessors

## Slide 17: Performance Study: Commercial Workload
Performance of Symmetric Shared-Memory Multiprocessors

## Slide 18: Performance Study: Commercial Workload
Performance of Symmetric Shared-Memory Multiprocessors

## Slide 19: Directory Protocols
Snooping schemes require communication among all caches on every cache miss
  Limits scalability
  Another approach: Use centralized directory to keep track of every block
    Which caches have each block
    Dirty status of each block
Implement in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
  Not scalable beyond shared L3
Distributed Shared Memory and Directory-Based Coherence

## Slide 20: Directory Protocols
Alternative approach:
  Distribute memory
Distributed Shared Memory and Directory-Based Coherence

## Slide 21: Directory Protocols
For each block, maintain state:
  Shared
    One or more nodes have the block cached, value in memory is up-to-date
    Set of node IDs
  Uncached
  Modified
    Exactly one node has a copy of the cache block, value in memory is out-of-date
    Owner node ID
Directory maintains block states and sends invalidation messages
Distributed Shared Memory and Directory-Based Coherence

## Slide 22: Messages
Distributed Shared Memory and Directory-Based Coherence

## Slide 23: Directory Protocols
Distributed Shared Memory and Directory-Based Coherence

## Slide 24: Directory Protocols
For uncached block:
  Read miss
    Requesting node is sent the requested data and is made the only sharing node, block is now shared
  Write miss
    The requesting node is sent the requested data and becomes the sharing node, block is now exclusive
For shared block:
  Read miss
    The requesting node is sent the requested data from memory, node is added to sharing set
  Write miss
    The requesting node is sent the value, all nodes in the sharing set are sent invalidate messages, sharing set only contains requesting node, block is now exclusive
Distributed Shared Memory and Directory-Based Coherence

## Slide 25: Directory Protocols
For exclusive block:
  Read miss
    The owner is sent a data fetch message, block becomes shared, owner sends data to the directory, data written back to memory, sharers set contains old owner and requestor
  Data write back
    Block becomes uncached, sharer set is empty
  Write miss
    Message is sent to old owner to invalidate and send the value to the directory, requestor becomes new owner, block remains exclusive
Distributed Shared Memory and Directory-Based Coherence

## Slide 26: Synchronization
Basic building blocks:
  Atomic exchange
    Swaps register with memory location
  Test-and-set
    Sets under condition
  Fetch-and-increment
    Reads original value from memory and increments it in memory
  Requires memory read and write in uninterruptable instruction
  RISC-V: load reserved/store conditional
    If the contents of the memory location specified by the load linked are changed before the store conditional to the same address, the store conditional fails
Synchronization

## Slide 27: Implementing Locks
Atomic exchange (EXCH):
try: mov x3,x4 ;mov exchange value
lr x2,x1 ;load reserved from
sc x3,0(x1) ;store conditional
bnez x3,try ;branch store fails
mov x4,x2 ;put load value in x4?
Atomic increment:
try: lr x2,x1 ;load reserved 0(x1)
addi x3,x2,1 ;increment
sc x3,0(x1) ;store conditional
bnez x3,try ;branch store fails
Synchronization

## Slide 28: Implementing Locks
Lock (no cache coherence)
addi x2,R0,#1
lockit: EXCH x2,0(x1) ;atomic exchange
bnez x2,locket ;already locked?
Lock (cache coherence):
lockit: ld x2,0(x1) ;load of lock
bnez x2,locket ;not available-spin
addi x2,R0,#1 ;load locked value
EXCH x2,0(x1) ;swap
bnez x2,locket ;branch if lock wasn’t 0
Synchronization

## Slide 29: Implementing Locks
Advantage of this scheme: reduces memory traffic
Synchronization

## Slide 30: Models of Memory Consistency
Models of Memory Consistency: An Introduction
Processor 1:
A=0
…
A=1
if (B==0) …
Processor 2:
B=0
…
B=1
if (A==0) …
Should be impossible for both if-statements to be evaluated as true
  Delayed write invalidate?
Sequential consistency:
  Result of execution should be the same as long as:
    Accesses on each processor were kept in order
    Accesses on different processors were arbitrarily interleaved

## Slide 31: Implementing Locks
To implement, delay completion of all memory accesses until all invalidations caused by the access are completed
  Reduces performance!
Alternatives:
  Program-enforced synchronization to force write on processor to occur before read on the other processor
    Requires synchronization object for A and another for B
      “Unlock” after write
      “Lock” after read
Models of Memory Consistency: An Introduction

## Slide 32: Relaxed Consistency Models
Rules:
  X → Y
    Operation X must complete before operation Y is done
    Sequential consistency requires:
      R → W, R → R, W → R, W → W
  Relax W → R
    “Total store ordering”
  Relax W → W
    “Partial store order”
  Relax R → W and R → R
    “Weak ordering” and “release consistency”
Models of Memory Consistency: An Introduction

## Slide 33: Relaxed Consistency Models
Models of Memory Consistency: An Introduction

## Slide 34: Relaxed Consistency Models
Consistency model is multiprocessor specific
Programmers will often implement explicit synchronization
Speculation gives much of the performance advantage of relaxed models with sequential consistency
  Basic idea: if an invalidation arrives for a result that has not been committed, use speculation recovery
Models of Memory Consistency: An Introduction

## Slide 35: Fallacies and Pitfalls
Measuring performance of multiprocessors by linear speedup versus execution time
Amdahl’s Law doesn’t apply to parallel computers
Linear speedups are needed to make multiprocessors cost-effective
  Doesn’t consider cost of other system components
Not developing the software to take advantage of, or optimize for, a multiprocessor architecture
Fallacies and Pitfalls