## Slide 1
Chapter 7
Domain-Specific Architectures
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Moore’s Law enabled:
  Deep memory hierarchy
  Wide SIMD units
  Deep pipelines
  Branch prediction
  Out-of-order execution
  Speculative prefetching
  Multithreading
  Multiprocessing
Objective:
  Extract performance from software that is oblivious to architecture
Introduction

## Slide 3: Introduction
Need factor of 100 improvements in number of operations per instruction
  Requires domain specific architectures
  For ASICs, NRE cannot be amoratized over large volumes
  FPGAs are less efficient than ASICs
Introduction

## Slide 4: Guidelines for DSAs
Use dedicated memories to minimize data movement
Invest resources into more arithmetic units or bigger memories
Use the easiest form of parallelism that matches the domain
Reduce data size and type to the simplest needed for the domain
Use a domain-specific programming language
Guidelines for DSAs

## Slide 5: Guidelines for DSAs
Guidelines for DSAs

## Slide 6: Example: Deep Neural Networks
Inpired by neuron of the brain
Computes non-linear “activiation” function of the weighted sum of input values
Neurons arranged in layers
Example: Deep Neural Networks

## Slide 7: Example: Deep Neural Networks
Most practioners will choose an existing design
  Topology
  Data type
Training (learning):
  Calculate weights using backpropagation algorithm
  Supervised learning: stocastic graduate descent
Inferrence: use neural network for classification
Example: Deep Neural Networks

## Slide 8: Multi-Layer Perceptrons
Parameters:
  Dim[i]: number of neurons
  Dim[i-1]: dimension of input vector
  Number of weights: Dim[i-1] x Dim[i]
  Operations: 2 x Dim[i-1] x Dim[i]
  Operations/weight: 2
Example: Deep Neural Networks

## Slide 9: Convolutional Neural Network
Computer vision
Each layer raises the level of abstraction
  First layer recognizes horizontal and vertical lines
  Second layer recognizes corners
  Third layer recognizes shapes
  Fourth layer recognizes features, such as ears of a dog
  Higher layers recognizes different breeds of dogs
Example: Deep Neural Networks

## Slide 10: Convolutional Neural Network
Parameters:
  DimFM[i-1]: Dimension of the (square) input Feature Map
  DimFM[i]: Dimension of the (square) output Feature Map
  DimSten[i]: Dimension of the (square) stencil
  NumFM[i-1]: Number of input Feature Maps
  NumFM[i]: Number of output Feature Maps
  Number of neurons: NumFM[i] x DimFM[i]2
  Number of weights per output Feature Map: NumFM[i-1] x DimSten[i]2
  Total number of weights per layer: NumFM[i] x Number of weights per output Feature Map
  Number of operations per output Feature Map: 2 x DimFM[i]2 x Number of weights per output Feature Map
  Total number of operations per layer: NumFM[i] x Number of operations per output Feature Map = 2 x DimFM[i]2 x NumFM[i] x Number of weights per output Feature Map = 2 x DimFM[i]2 x Total number of weights per layer
  Operations/Weight: 2 x DimFM[i]2
Example: Deep Neural Networks

## Slide 11: Recurrent Neural Network
Speech recognition and language translation
Long short-term memory (LSTM) network
Example: Deep Neural Networks

## Slide 12: Recurrent Neural Network
Example: Deep Neural Networks
Parameters:
  Number of weights per cell: 3 x (3 x Dim x Dim)+(2 x Dim x Dim) + (1 x Dim x Dim) = 12 x Dim2
  Number of operations for the 5 vector-matrix multiplies per cell: 2 x Number of weights per cell = 24 x Dim2
  Number of operations for the 3 element-wise multiplies and 1 addition (vectors are all the size of the output): 4 x Dim
  Total number of operations per cell (5 vector-matrix multiplies and the 4 element-wise operations): 24 x Dim2 + 4 x Dim
  Operations/Weight: ~2

## Slide 13: Convolutional Neural Network
Batches:
  Reuse weights once fetched from memory across multiple inputs
  Increases operational intensity
Quantization
  Use 8- or 16-bit fixed point
Summary:
  Need the following kernels:
    Matrix-vector multiply
    Matrix-matrix multiply
    Stencil
    ReLU
    Sigmoid
    Hyperbolic tangeant
Example: Deep Neural Networks

## Slide 14: Tensor Processing Unit
Google’s DNN ASIC
256 x 256 8-bit matrix multiply unit
Large software-managed scratchpad
Coprocessor on the PCIe bus
Tensor Processing Unit

## Slide 15: Tensor Processing Unit
Tensor Processing Unit

## Slide 16: TPU ISA
Read_Host_Memory
  Reads memory from the CPU memory into the unified buffer
Read_Weights
  Reads weights from the Weight Memory into the Weight FIFO as input to the Matrix Unit
MatrixMatrixMultiply/Convolve
  Perform a matrix-matrix multiply, a vector-matrix multiply, an element-wise matrix multiply, an element-wise vector multiply, or a convolution from the Unified Buffer into the accumulators
  takes a variable-sized B*256 input, multiplies it by a 256x256 constant input, and produces a B*256 output, taking B pipelined cycles to complete
Activate
  Computes activation function
Write_Host_Memory
  Writes data from unified buffer into host memory
Tensor Processing Unit

## Slide 17: TPU ISA
Tensor Processing Unit

## Slide 18: TPU ISA
Tensor Processing Unit

## Slide 19: TPU ISA
Read_Host_Memory
  Reads memory from the CPU memory into the unified buffer
Read_Weights
  Reads weights from the Weight Memory into the Weight FIFO as input to the Matrix Unit
MatrixMatrixMultiply/Convolve
  Perform a matrix-matrix multiply, a vector-matrix multiply, an element-wise matrix multiply, an element-wise vector multiply, or a convolution from the Unified Buffer into the accumulators
  takes a variable-sized B*256 input, multiplies it by a 256x256 constant input, and produces a B*256 output, taking B pipelined cycles to complete
Activate
  Computes activation function
Write_Host_Memory
  Writes data from unified buffer into host memory
Tensor Processing Unit

## Slide 20: Improving the TPU
Tensor Processing Unit

## Slide 21: The TPU and the Guidelines
Use dedicated memories
  24 MiB dedicated buffer, 4 MiB accumulator buffers
Invest resources in arithmetic units and dedicated memories
  60% of the memory and 250X the arithmetic units of a server-class CPU
Use the easiest form of parallelism that matches the domain
  Exploits 2D SIMD parallelism
Reduce the data size and type needed for the domain
  Primarily uses 8-bit integers
Use a domain-specific programming language
  Uses TensorFlow
Tensor Processing Unit

## Slide 22: Microsoft Catapult
Needed to be general purpose and power efficient
  Uses FPGA PCIe board with dedicated 20 Gbps network in 6 x 8 torus
  Each of the 48 servers in half the rack has a Catapult board
  Limited to 25 watts
  32 MiB Flash memory
  Two banks of DDR3-1600 (11 GB/s) and 8 GiB DRAM
  FPGA (unconfigured) has 3962 18-bit ALUs and 5 MiB of on-chip memory
  Programmed in Verilog RTL
  Shell is 23% of the FPGA
Microsoft Capapult

## Slide 23: Microsoft Catapult: CNN
CNN accelerator, mapped across multiple FPGAs
Microsoft Capapult

## Slide 24: Microsoft Catapult: CNN
Microsoft Capapult

## Slide 25: Microsoft Catapult: Search Ranking
Microsoft Capapult
Feature extraction (1 FPGA)
  Extracts 4500 features for every document-query pair, e.g. frequency in which the query appears in the page
  Systolic array of FSMs
Free-form expressions (2 FPGAs)
  Calculates feature combinations
Machine-learned Scoring (1 FPGA for compression, 3 FPGAs calculate score)
  Uses results of previous two stages to calculate floating-point score
One FPGA allocated as a hot-spare

## Slide 26: Microsoft Catapult: Search Ranking
Microsoft Capapult
Free-form expression evaluation
  60 core processor
  Pipelined cores
  Each core supports four threads that can hide each other’s latency
  Threads are statically prioritized according to thread latency

## Slide 27: Microsoft Catapult: Search Ranking
Microsoft Capapult
Version 2 of Catapult
  Placed the FPGA between the CPU and NIC
  Increased network from 10 Gb/s to 40 Gb/s
  Also performs network acceleration
  Shell now consumes 44% of the FPGA
  Now FPGA performs only feature extraction

## Slide 28: Catapult and the Guidelines
Microsoft Capapult
Use dedicated memories
  5 MiB dedicated memory
Invest resources in arithmetic units and dedicated memories
  3926 ALUs
Use the easiest form of parallelism that matches the domain
  2D SIMD for CNN, MISD parallelism for search scoring
Reduce the data size and type needed for the domain
  Uses mixture of 8-bit integers and 64-bit floating-point
Use a domain-specific programming language
  Uses Verilog RTL; Microsoft did not follow this guideline

## Slide 29: Intel Crest
Intel Crest
DNN training
16-bit fixed point
Operates on blocks of 32x32 matrices
SRAM + HBM2

## Slide 30: Pixel Visual Core
Pixel Visual Core
Pixel Visual Core
  Image Processing Unit
  Performs stencil operations
  Decended from Image Signal processor

## Slide 31: Pixel Visual Core
Software written in Halide, a DSL
  Compiled to virtual ISA
  vISA is lowered to physical ISA using application-specific parameters
  pISA is VLSI
Optimized for energy
  Power Budget is 6 to 8 W for bursts of 10-20 seconds, dropping to tens of milliwatts when not in use
  8-bit DRAM access equivalent energy as 12,500 8-bit integer operations or 7 to 100 8-bit SRAM accesses
  IEEE 754 operations require 22X to 150X of the cost of 8-bit integer operations
Optimized for 2D access
  2D SIMD unit
  On-chip SRAM structured using a square geometry
Pixel Visual Core

## Slide 32: Pixel Visual Core
Pixel Visual Core

## Slide 33: Pixel Visual Core
Pixel Visual Core

## Slide 34: Pixel Visual Core
Pixel Visual Core

## Slide 35: Visual Core and the Guidelines
Microsoft Capapult
Use dedicated memories
  128 + 64 MiB dedicated memory per core
Invest resources in arithmetic units and dedicated memories
  16x16 2D array of processing elements per core and 2D shifting network per core
Use the easiest form of parallelism that matches the domain
  2D SIMD and VLIW
Reduce the data size and type needed for the domain
  Uses mixture of 8-bit and 16-bit integers
Use a domain-specific programming language
  Halide for image processing and TensorFlow for CNNs

## Slide 36: Fallacies and Pitfalls
Microsoft Capapult
It costs $100 million to design a custom chip
Performance counters added as an afterthought
Architects are tackling the right DNN tasks
For DNN hardware, inferences per second (IPS) is a fair summary performance metric
Being ignorant of architecture history when designing an DSA