## Slide 1: Gates and Boolean Algebra
Ch 3.1

## Slide 2: Gates
Digital circuit is one in which only two logical values are present
Different values represented by varying signals
  Signal between 0 and 0.5 volts (often binary/logical 0)
  Signal between 1 and 1.5 volts (often binary/logical 1)
Voltages outside those ranges not permitted
Gates: tiny electronic devices that compute various functions of these two-valued signals
  Form the hardwire basis on which all digital computers are built
  Details of how gates work inside is the device level: beyond our scope (below our level 0)

## Slide 3
(a) A transistor inverter. (b) A NAND gate. (c) A NOR gate.
Gates at the device level … very briefly
Input (Vin, or V1, V2) & output voltage (Vout)
When input voltage is low (below a certain critical value)
  transistor turns off and acts like an infinite resistance
  Vout is high: takes on value close to Vcc (typically +1.5 volts -- logical 1)
When input voltage is high (exceeds critical value)
  transistor switches on and acts like a wire
  Vout is low: pulled down to ground (0 volts -- logical 0)
Output is 0 iff both inputs are 1
Converts logical 0 into logical 1, and vice versa
Output is 1 iff both inputs are 0

## Slide 4
The three simplest gates: NOT, NAND, NOR
We will represent gates as symbols
Small circles in the gate are called inversion bubbles
Gate symbols:
Boolean function: (described by a truth table)

## Slide 5
Two additional gates: AND, OR
We will represent gates as symbols
Small circles in the gate are called inversion bubbles
Gate symbols (top)
Boolean function (bottom - described by a truth table)

## Slide 6
Two additional gates: AND, OR
We will represent gates as symbols
Small circles in the gate are called inversion bubbles
Gate symbols (top)
Boolean function (bottom - described by a truth table)
Q: How many transistors does each gate require?

## Slide 7
Boolean algebra
Variables and functions can take on only the values 0 and 1
Ex: Boolean function f is defined as f(A) = 1 if A is 0, and f(A) = 0 if A is 1.
  NOT function
How many possible combinations of input values are possible in a Boolean function of n variables?

## Slide 8
Boolean algebra
Variables and functions can take on only the values 0 and 1
Ex: Boolean function f is defined as f(A) = 1 if A is 0, and f(A) = 0 if A is 1.
  NOT function
How many possible combinations of input values are possible in a Boolean function of n variables?
Truth table: A way of completely describing a Boolean function by giving a table with rows, each row telling the value of the function for a different combination of input values.
  List rows in ascending numerical order (base 2)
  First row: all 0s
  Last row: all 1s
We can describe a function by reading the result column of the truth table vertically.
  Ex: NAND is 1110

## Slide 9
Boolean function notation
Suppose there is one inputs to a function f, which we will call A.
The NOT function can be described as
Suppose there are two inputs to a function f, which we will call A and B.
The OR function can be described as
The AND function can be described as

## Slide 10
Boolean function notation
Suppose there is one inputs to a function f, which we will call A.
The NOT function can be described as
Suppose there are two inputs to a function f, which we will call A and B.
The OR function can be described as
The AND function can be described as
Here, we have a function f with three inputs A,B,C.
This is the majority logic function, i.e.,
it is 0 if a majority of its inputs are 0, and
It is 1 if a majority of its inputs are 1
We could describe this function by: 1) its truth table, or
2) the following compact representation:

## Slide 11
Constructing a circuit for a function
Input: a Boolean function (majority function of 3 variables) as described in the following truth table.
Goal: Draw a circuit that accomplishes this using only AND, OR, and NOT gates.

## Slide 12
Constructing a circuit for a function
Input: a Boolean function (majority function of 3 variables) as described in the following truth table.
Goal: Draw a circuit that accomplishes this using only AND, OR, and NOT gates.

## Slide 13: Circuit implementation
We have a general method to implement a circuit for any Boolean function:
Write truth table for function
Provide inverters to generate complement of each input
Draw AND gate for each term with 1 in result column
Wire AND gates to appropriate inputs
Feed output of all AND gates into an OR gate
Example: Implement a circuit for Boolean function f which takes three inputs, A, B, C, and outputs a 1 iff no more than one of the inputs is a 1.

## Slide 14: Ex: Circuit implementation
Example: Implement a circuit for Boolean function f which takes three inputs, A, B, C, and outputs a 1 iff no more than one of the inputs is a 1.

## Slide 15: Working towards a better circuit implementation
New goal: Construct a circuit with less gates
  Reduce chip area needed to implement them
  Minimize power consumption
  Increase speed
Our previous approach guarantees we CAN construct a circuit
  Solution is feasible
  Doesn’t necessarily construct one using only a few gates
A functionally complete set of gates is one which can be used to express all possible truth tables by combining members of the set into a Boolean expression.
  {NOT, AND, OR} is functionally complete.
  {NAND} is functionally complete.
  {NOR} is functionally complete.
It’s often convenient to implement circuits using only a single type of gate
  Ex: any Boolean function can be computed using just NAND gates! (or just NOR gates!)

## Slide 16: Circuit equivalence: NOT, AND, and OR using only NAND gates
Which one is which?

## Slide 17: Circuit equivalence: NOT, AND, and OR using only NOR gates
Which one is which?

## Slide 18: Circuit Equivalence
Goal: Design a circuit using a small number of gates
  Reduces chip area needed
  Minimizes power consumption
  Increases speed
Example: Can you find a circuit which uses less gates but is equivalent to the circuit on the right? Note: Use a truth table to prove equivalence.
Two circuits/functions are equivalent if and only if they have the same output for every possible input.

## Slide 19: Identities of Boolean Algebra

## Slide 20: Gate Equivalence of De Morgan’s law

## Slide 21: Examples
Build a circuit for XOR. Can you build it in more than one way?
Use a truth table to show that X = (X AND Y) OR (X AND NOT Y)

## Slide 22: Note on equivalence: Positive vs. Negative logic
The same physical gate can compute different functions, depending on the convention used.
Electrical Positive logic Negative logic characteristics of a device
Negative logic:
low voltage = logical 1 / true
high voltage = logical 0 / false
Positive logic: (we assume this)
low voltage = logical 0 / false
high voltage = logical 1 / true

## Slide 23: Example circuit: Half-Adder (Fig 3-16)
Goal: Add A+B
Output: Sum and Carry
A circuit for a half adder.
Truth table for 1-bit addition.