## Slide 1: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 2: 2s-Complement Signed Integers
For nonnegative n:
Use ordinary base-two representation with leading (sign) bit 0
For negative n (–n):
(1) Find w-bit base-2 representation of n
(2) Complement each bit
(3) Add 1 (Flip all bits from rightmost 0 to the end)
Example: –88
1. 88 as a 16-bit base-two number
2. Complement this bit string
3. Add 1
0000000001011000
1111111110100111
1111111110101000

## Slide 3: Why 2s-Complement
Sign Magnitude: One’s Two's 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: balance, number of zeros, ease of operations
Which one is best? Why?

## Slide 4: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 5: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 6: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 7: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action

## Slide 8: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video

## Slide 9: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 10: Multiplication Hardware
Initially 0

## Slide 11: Multiplication Hardware
Multiply 2 (0010) by 3(0011)

## Slide 12: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 13: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 14: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 15: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 16: Division Hardware
Initially dividend
Initially divisor in left half
Initially 0

## Slide 17: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 18: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps

## Slide 19: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 20: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 21: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 22: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 23: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 24: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 25: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 26: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 27: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 28: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 29: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 30: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 31: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 32: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 33: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 34: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 35: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 36: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 37: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)

## Slide 38: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, …)
  Sets or clears FP condition-code bit
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel

## Slide 39: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) lwc2 $f18, const9($gp) div.s $f16, $f16, $f18 lwc1 $f18, const32($gp) sub.s $f18, $f12, $f18 mul.s $f0, $f16, $f18 jr $ra

## Slide 40: FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k; for (i = 0; i! = 32; i = i + 1) for (j = 0; j! = 32; j = j + 1) for (k = 0; k! = 32; k = k + 1) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2

## Slide 41: FP Example: Array Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …

## Slide 42: FP Example: Array Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1

## Slide 43: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 44: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)
§3.6 Parallelism and Computer Arithmetic: Subword Parallelism

## Slide 45: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance
§3.7 Real Stuff: Streaming SIMD Extensions and AVX in x86

## Slide 46: x86 FP Instructions
Optional variations
  I: integer operand
  P: pop operand from stack
  R: reverse operand order
  But not all combinations allowed
Data transfer | Arithmetic | Compare | Transcendental
FILD mem/ST(i) FISTP mem/ST(i) FLDPI FLD1 FLDZ | FIADDP mem/ST(i) FISUBRP mem/ST(i) FIMULP mem/ST(i) FIDIVRP mem/ST(i) FSQRT FABS FRNDINT | FICOMP FIUCOMP FSTSW AX/mem | FPATAN F2XMI FCOS FPTAN FPREM FPSIN FYL2X

## Slide 47: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data

## Slide 48: Matrix Multiply
Unoptimized code:
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n]; /* cij = C[i][j] */
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n]; /* cij += A[i][k]*B[k][j] */
9. C[i+j*n] = cij; /* C[i][j] = cij */
10. }
11. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply

## Slide 49: Matrix Multiply
x86 assembly code:
1. vmovsd (%r10),%xmm0 # Load 1 element of C into %xmm0
2. mov %rsi,%rcx # register %rcx = %rsi
3. xor %eax,%eax # register %eax = 0
4. vmovsd (%rcx),%xmm1 # Load 1 element of B into %xmm1
5. add %r9,%rcx # register %rcx = %rcx + %r9
6. vmulsd (%r8,%rax,8),%xmm1,%xmm1 # Multiply %xmm1, element of A
7. add $0x1,%rax # register %rax = %rax + 1
8. cmp %eax,%edi # compare %eax to %edi
9. vaddsd %xmm1,%xmm0,%xmm0 # Add %xmm1, %xmm0
10. jg 30 <dgemm+0x30> # jump if %eax > %edi
11. add $0x1,%r11d # register %r11 = %r11 + 1
12. vmovsd %xmm0,(%r10) # Store %xmm0 into C element
§3.8 Going Faster: Subword Parallelism and Matrix Multiply

## Slide 50: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i+=4 )
5. for ( int j = 0; j < n; j++ ) {
6. __m256d c0 = _mm256_load_pd(C+i+j*n); /* c0 = C[i][j] */
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, /* c0 += A[i][k]*B[k][j] */
9. _mm256_mul_pd(_mm256_load_pd(A+i+k*n),
10. _mm256_broadcast_sd(B+k+j*n)));
11. _mm256_store_pd(C+i+j*n, c0); /* C[i][j] = c0 */
12. }
13. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply

## Slide 51: Matrix Multiply
Optimized x86 assembly code:
1. vmovapd (%r11),%ymm0 # Load 4 elements of C into %ymm0
2. mov %rbx,%rcx # register %rcx = %rbx
3. xor %eax,%eax # register %eax = 0
4. vbroadcastsd (%rax,%r8,1),%ymm1 # Make 4 copies of B element
5. add $0x8,%rax # register %rax = %rax + 8
6. vmulpd (%rcx),%ymm1,%ymm1 # Parallel mul %ymm1,4 A elements
7. add %r9,%rcx # register %rcx = %rcx + %r9
8. cmp %r10,%rax # compare %r10 to %rax
9. vaddpd %ymm1,%ymm0,%ymm0 # Parallel add %ymm1, %ymm0
10. jne 50 <dgemm+0x50> # jump if not %r10 != %rax
11. add $0x1,%esi # register % esi = % esi + 1
12. vmovapd %ymm0,(%r11) # Store %ymm0 into 4 C elements
§3.8 Going Faster: Subword Parallelism and Matrix Multiply

## Slide 52: Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  c.f. 111110112 >>> 2 = 001111102 = +62
§3.9 Fallacies and Pitfalls

## Slide 53: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 54: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles

## Slide 55: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
§3.9 Concluding Remarks

## Slide 56: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow
MIPS ISA
  Core instructions: 54 most frequently used
    100% of SPECINT, 97% of SPECFP
  Other instructions: less frequent